## Slide 1: Protocols

## Slide 2: Protocol
When computers communicate with each other, there needs to be a common set of rules and instructions that each computer follows. A specific set of communication rules is called a protocol.
A network protocol defines rules and conventions for communication between network devices.
Network protocols include mechanisms for devices to identify and make connections with each other.

## Slide 3: Some Protocols
DHCP
DNS
HTTP
FTP
SMTP
SNMP
TCP
UDP
IP
ARP
ICMP
IGMP
Telnet
PPP
POP
IMAP
SLIP
SSH

## Slide 4: DHCP
Dynamic Host Configuration Protocol (DHCP) is a client/server protocol that automatically provides an Internet Protocol (IP) host with its IP address and other related configuration information such as the subnet mask and default gateway.
DHCP allows hosts to obtain required TCP/IP configuration information from a DHCP server.

## Slide 5: DNS
Domain Name System (or Service or Server), an Internet service that translates domain names into IP addresses. Because domain names are alphabetic, they're easier to remember. The Internet however, is really based on IP addresses.
Purpose of DNS is to translate domain names into IP addresses
DNS services can used in public Network (Internet) and as well as Private Network.

## Slide 6: HTTP
HTTP means Hyper Text Transfer Protocol. HTTP is the underlying protocol used by the World Wide Web and this protocol defines how messages are formatted and transmitted, and what actions Web servers and browsers should take in response to various commands.
For example, when you enter a URL in your browser, this actually sends an HTTP command to the Web server directing it to fetch and transmit the requested Web page.

## Slide 7: FTP
File Transfer Protocol (FTP) is the commonly used protocol for exchanging files over the Internet. FTP uses the Internet's TCP/IP protocols to enable data transfer. FTP uses a client-server architecture, often secured with SSL/TLS.
FTP promotes sharing of files via remote computers with reliable and efficient data transfer

## Slide 8: SMTP
Simple Mail Transfer Protocol, a protocol for sending e-mail messages between servers. Most e-mail systems that send mail over the Internet use SMTP to send messages from one server to another; the messages can then be retrieved with an e-mail client using either POP or IMAP.
SMTP is generally used to send messages from a mail client to a mail server.

## Slide 9: SNMP
Simple Network Management Protocol (SNMP) is a popular protocol for network management. It is used for collecting information from, and configuring, network devices, such as servers, printers, hubs, switches, and routers on an Internet Protocol (IP) network.
SNMP is one of the widely accepted protocols to manage and monitor network elements.

## Slide 10: TCP [Transmission Control Protocol]
TCP is one of the main protocols in TCP/IP networks. Whereas the IP protocol deals only with packets, TCP enables two hosts to establish a connection and exchange streams of data. TCP guarantees delivery of data and also guarantees that packets will be delivered in the same order in which they were sent.
TCP[ Transmission Control Protocol] is a reliable protocol.

## Slide 11: UDP [User Datagram Protocol]
UDP is a connectionless protocol that runs on top of IP networks. Unlike TCP/IP, UDP/IP provides very few error recovery services, offering instead a direct way to send and receive datagrams over an IP network.
UDP is used to send short messages called datagrams but overall, it is an unreliable, connectionless protocol.

## Slide 12: IP [Internet Protocol]
The Internet Protocol (IP) is the method or protocol by which data is sent from one computer to another on the Internet. Each computer (known as a host) on the Internet has at least one IP address that uniquely identifies it from all other computers on the Internet.

## Slide 13: ARP
Address Resolution Protocol, a network layer protocol used to convert an IP address into a physical address (called a DLC address), such as an Ethernet address.
There is also Reverse ARP (RARP)which can be used by a host to discover its IP address. In this case, the host broadcasts its physical address and a RARP server replies with the host's IP address.

## Slide 14: ICMP
Internet Control Message Protocol is an extension to the Internet Protocol (IP). ICMP supports packets containing error, control, and informational messages.
It is an error reporting protocol and is used by routers, hosts and network devices to generate error messages when there are problems delivering IP packets.

## Slide 15: IGMP
The Internet Group Management Protocol (IGMP) is a communications protocol used by hosts and routers on IPv4 networks to establish multicast group memberships. IGMP is an integral part of IP multicast.
IGMP can be used for one-to-many networking applications such as online streaming video and gaming.
IGMP is used on IPv4 networks.

## Slide 16: Telnet
Telnet (short for Terminal NETwork) is a network protocol used to provide a command line interface for communicating with a device.
Telnet is a user command and an underlying TCP/IP protocol for accessing remote computers.
Through Telnet, an administrator or another user can access someone else's computer remotely.
Telnet is sometimes written in uppercase as TELNET and may also be misspelled as Telenet.

## Slide 17: PPP
Point-to-point protocol (PPP) is a computer network protocol used to transfer a datagram between two directly connected (point-to-point) computers. This protocol is used for a very basic level of connectivity providing data linkage between the computers.
PPP is most commonly used data link protocol. It is used to connect the Home PC to the server of ISP via a modem.
Point-to-point protocol is widely used for the heavier and faster connections necessary for broadband communications.

## Slide 18: POP
Post Office Protocol (POP) is a type of computer networking and Internet standard protocol that extracts and retrieves email from a remote mail server for access by the host machine.
POP is an application layer protocol in the OSI model that provides end users the ability to fetch and receive email.
Post Office Protocol is the primary protocol behind email communication.

## Slide 19: IMAP
The Internet Message Access Protocol (IMAP) is a mail protocol used for accessing email on a remote web server from a local client.
IMAP is an application layer Internet Protocol using the underlying transport layer protocols to establish host-to-host communication services for applications.
The IMAP architecture enables users to send and receive emails through a remote server, without support from a particular device.

## Slide 20: SLIP
SLIP is a TCP/IP protocol used for communication between two machines that are previously configured for communication with each other.
Serial Line Internet Protocol, a protocol for connection to the Internet via a dial-up connection.
A more common protocol is PPP (Point-to-Point Protocol) because it is faster and more reliable and supports functions that SLIP does not, such as error detection, dynamic assignment of IP addresses and data compression.

## Slide 21: SSH
SSH, also known as Secure Socket Shell, is a network protocol that provides administrators with a secure way to access a remote computer.
SSH also refers to the suite of utilities that implement the protocol.
Secure Shell provides strong authentication and secure encrypted data communications between two computers connecting over an insecure network such as the Internet.