## Slide 1: Computer Network
Internet Connection

## Slide 2: Dial-Up Connection
A dial-up connection uses a standard phone line and analog modem to access the Internet at data transfer rates (DTR) of up to 56 Kbps.
A dial-up connection is the least expensive way to access the Internet, but it also slowest connection.

## Slide 3: Dial-up Connection
A dial-up connection is established when two or more communication devices use a public switched telephone network (PSTN) to connect to an Internet service provider (ISP).
Many remote areas depend on Internet dial-up connections because broadband and cable are rare in remote areas with low population numbers.
ISPs often provide free dial-up connections, a viable alternative for budget-conscious subscribers.

## Slide 4: ISDN (Integrated Services Digital Network)
An ISDN is an international communications standard used for sending voice, video, and data over digital telephone lines or normal telephone wires. ISDN supports data transfer rates of 64 Kbps (64,000 bits per second).
There are two level of Service:
Basic Rate Interface (BRI): Intended for the home and small enterprise.
Primary Rate Interface (PRI): Intended for larger users.

## Slide 5: ADSL (Asymmetric Digital Subscriber Line)
Asymmetric digital subscriber line (ADSL) is a type of DSL broadband communications technology used for connecting to the Internet. ADSL allows more data to be sent over existing copper telephone lines (POTS), when compared to traditional modem lines.
ADSL requires a special ADSL modem and subscribers must be in close geographical locations to the provider's central office to receive ADSL service. Typically this distance is within a radius of 2 to 2.5 miles. ADSL supports data rates of from 1.5 to 9 Mbps when receiving data (known as the downstream rate) and from 16 to 640 Kbps when sending data (known as the upstream rate).

## Slide 6: Leased Line Connection
A leased line, also known as a dedicated line, connects two locations for private voice and data telecommunication service. A leased line is not a dedicated cable; it is a reserved circuit between two points. The leased line is always active and available for a fixed monthly fee.
Leased lines are most commonly rented by businesses to connect branch offices of the organization.

## Slide 7: Satellite Connection
A satellite Internet connection is an arrangement in which the upstream (outgoing) and the downstream (incoming) data are sent from, and arrive at, a computer through a satellite. Each subscriber's hardware includes a satellite dish antenna and a transceiver (transmitter/receiver) that operates in the microwave portion of the radio spectrum.

## Slide 8: FDDI (Fiber Distributed Data Interface)
FDDI (Fiber Distributed Data Interface) is a set of ANSI and ISO standards for data transmission on fiber optic lines in a local area network (LAN) that can extend in range up to 200 km (124 miles). The FDDI protocol is based on the token ring protocol. In addition to being large geographically, an FDDI local area network can support thousands of users. FDDI is frequently used on the backbone for a wide area network (WAN).