## Slide 1: Quality of Services
By
Dr Yasir Afaq

## Slide 2: Quality of Services
Quality-of-Service (QoS) refers to traffic control mechanisms that seek to either differentiate performance based on application or network-operator requirements or provide predictable or guaranteed performance to applications, sessions, or traffic aggregates.
Basic phenomenon for QoS means in terms of packet delay and losses of various kinds.

## Slide 3: Need for QoS –
Video and audio conferencing require bounded delay and loss rate.
Video and audio streaming requires bounded packet loss rate, it may not be so sensitive to delay.
Time-critical applications (real-time control) in which bounded delay is considered to be an important factor.
Valuable applications should be provided better services than less valuable applications.

## Slide 4: QoS Specification –
QoS requirements can be specified as:
Delay
Delay Variation(Jitter)
Throughput
Error Rate

## Slide 5: Solution
There are two types of QoS Solutions:
Stateless Solutions –
Routers maintain no fine-grained state about traffic, one positive factor of it is that it is scalable and robust. But it has weak services as there is no guarantee about the kind of delay or performance in a particular application which we have to encounter.
Stateful Solutions
Routers maintain a per-flow state as flow is very important in providing the Quality-of-Service i.e. providing powerful services such as guaranteed services and high resource utilization, providing protection, and is much less scalable and robust.

## Slide 6: Techniques for Quality of Service :
Overprovisioning The logic of overprovisioning is to provide greater router capacity, buffer space and bandwidth. It is an expensive technique as the resources are costly. Eg: Telephone System.
Buffering
Flows can be buffered on the receiving side before being delivered. It will not affect reliability or bandwidth, but helps to smooth out jitter. This technique can be used at uniform intervals.
Traffic Shaping –
It is defined as about regulating the average rate of data transmission.
It smooths the traffic on server side other than client side.
When a connection is set up, the user machine and subnet agree on a certain traffic pattern for that circuit called as Service Level Agreement.
It reduces congestion and thus helps the carrier to deliver the packets in the agreed pattern.